TYPICAL SPECIFICATION

Armstrong Vertical MultiStage Pressure Booster Systems

General

Furnish and install, as shown on the plans and specifications, an Armstrong Series 6800 Packaged Booster System designed for a total system capacity of ______ USgpm (L/s) with a total discharge head of _____ psi (kPa), including a minimum suction pressure of _____ psi (kPa).

Pumps

The pumps shall be Armstrong Series 4700 Vertical MultiStage, complete with stainless steel impellers, mechanical seal, PN16/PN25/125 psi/250 psi suction and discharge flanges. Pumps shall be mounted with squirrel cage induction motors suitable for operation with _____ Volt, 3 Phase, 50/60 Hz power supply.

Pumping Details

P1 Size:  _____, Flow: _____ USgpm (L/s), at _____ feet of head (kPa) with _____ hp (kW), 2900/3560 rpm motor.

P2 Size:  _____, Flow: _____ USgpm (L/s), at _____ feet of head (kPa) with _____ hp (kW), 2900/3560 rpm motor.

P3 Size:  _____, Flow: _____ USgpm (L/s), at _____ feet of head (kPa) with _____ hp (kW), 2900/3560 rpm motor.

P4 Size:  _____, Flow: _____ USgpm (L/s), at _____ feet of head (kPa) with _____ hp (kW), 2900/3560 rpm motor.

Assembly

All headers and interconnecting piping shall be stainless steel or copper. Common suction and discharge headers shall have threaded ends or flange adapters. The assembly shall be complete with full port ball valves, check valves and pressure gauges. ASME or BS4814 hydro-accumulator shall be package mounted to allow shutdown during periods of no demand.

Control Panel

The control panel shall be of the pressure switch/microprocessor/variable speed type. The complete control panel assembly and all the internal devices shall be UL508, CSA or CE labeled. The panel shall be complete with IP54/NEMA 1 enclosure and include door interlocked main disconnect and magnetic motor starters with fused motor protectors, adjustable time delays, Hand-Off-Auto selector switch for each pump, power on light, minimum run timers, low suction pressure switch and pilot light. The control circuit shall include fault relay circuit to turn on the next pump should the lead pump fail.

Testing

The system shall be factory assembled, wired, performance tested, calibrated and shipped ready to receive piping and wiring. The entire package shall be manufactured at an ISO 9001 manufacturing facility and available with UL packaged system certification.