Containerized Fire System

Typical Specifications

Armstrong– Containerized Fire System

- 100% factory assembled and tested at ISO certified facility.

- Ventilation with exhaust fans to control internal temperature and enough air supply to Engine

- Assembled in ISO standard shipping containers.

- Controls and piping per NFPA 20 requirements.

- Internal Fire sprinkler as per NFPA 13 as Optional

- UL/FM approved pumps and accessories wherever applicable

- Double cargo door and separate entry door for easy access.

- Available with diesel or electric fire pumps.

- Both 20 ft and 40 ft containers available, depending on equipment needs

- Container dimensions allow for any size or type of Armstrong fire solution.

- Rated for outdoor and/or marine environment installations

- Piping drain points drain water to exterior

- Common floor drain for cleaning

- Non-slip, checkered flooring plates

- Professionally designed using 3-D CAD modeling software

- Designs adhere to regional industry codes.

# Text boxes

File No: F46.131

Date: March 13, 2019

Supersedes: New

Date: New